## Slide 1: SRS Calibration Part II: Dynamic Range, Signal/Noise, Pulse Shape and Timing Jitter + initial results from scan of FIT zigzag board
Michael Phipps, Bob Azmoun, Craig Woody

## Slide 2: Muxgain: Signal/Noise
** For better signal to noise, use Muxgain 3 (which is really Muxgain 4)
-
Mux 1
Mux 2
Mux 3
Mux 4
Fe55 Spectrum: Peripheral pad from highly collimated xray gun

## Slide 3: Muxgain: Dynamic Range
** For better dynamic range, use Muxgain 1
- IMUXIN of 0x01 is safest location for pedestal
Fe55 spectrum across all pads for scaled Muxgains
Peripheral primary peak
- Scale the spectrum for each Muxgain from the mean of this peak
Primary Fe55 peak in center of cluster
- Falls at edge of saturation, so convenient measure of dynamic range

## Slide 4: Nonlinearity Curves
Mux 1: Best dynamic range
Mux 4: Used in the past
Correct by linear fit after kink
If anyone wants the root file, just let me know

## Slide 5: Characteristic SRS Pulse Shape: Internal APV pulser, post-nonlinearity correction
- Characteristic pulse shape from the APV shaper
- Alexander has used this expected pulse to deconvolve FBTF signals from multiple ionization events

## Slide 6: SRS Timing Jitter: +- 12.5 ns?
UVA’s external pulser tests
Internal FEC clock has 25 ns period
Shows up as a jitter in peak timing bin relative to the trigger
Max time bin is a function of injected charge
In test beam data, these plots show broader distribution from ionization statistical effects
May be possible to partially recover absolute clock by fitting rising edge of signal and normalizing z coordinate
BNL external pulser tests across virtual capacitor: similar to UVA results
~1150 ADC
~1100 ADC